## Slide 1: Vehicle and Pedestrian Detection Technologies
Virtual Traffic Engineering and Safety Conference
October 22, 2020
1

## Slide 2: Presenters
2

## Slide 3: History of Detection for What?
Security
Traffic signal intersection control
Incident
Vehicle counting
Pedestrian counting
3

## Slide 4
The vehicle in 1995
How did Intelligent Transportation Systems see the vehicles 25 years ago?
Metal-reflection
Video Pixel Changes
Weight/pressure
Metal magnetic field presence
Vehicle shapes
Engine Acoustics
Heat
License Plates
4

## Slide 5
Mobile phones:
Bluetooth
GSM
Vehicle Diagnostics:
Bluetooth
Hands free-sets:
Bluetooth
GPS Navigation Systems:
Bluetooth Floating Vehicle (GPRS)
Portable PC / PDA:
Bluetooth
WiFi
V2X Communication:
Vehicle Tags:
RFID
Micro wave
Bluetooth
The vehicle in 2020
How do the new Intelligent Transportation Systems see the vehicles today?
5

## Slide 6: Brief History
What technologies have been used?
  Sound
  Treadles
  Inductive loop
  Ultrasonic – Radar, Microwave
  Magnetic
  Video imagining
  Thermal Imaging
6

## Slide 7: Signal Intersection Control
7

## Slide 8: Signal Intersection Control
Inductive loops
  Only detects metal Objects
8

## Slide 9: LOOP Detectors – Ramp Metering
9

## Slide 10: Inductive Loop
Advantages
  Accurate
  Accepted technology
  Field proven
  Installation requires no new equipment
Disadvantages
  Labor intensive to install
  Requires traffic control to install
  No ability to relocate
  Pavement life determines loop life
  Needs to be on diggers hotline
10

## Slide 11
Microwave Detection
11

## Slide 12
Microwave Detection Advancements and Combo
12

## Slide 13
      Advantages
        Low cost
        Easy to install
        Aim for zone
      Disadvantages
        Unpredictable zone coverage
        Limited range
        Need for fixed mounting
        Presence detection requires logic
Microwave Detection
13

## Slide 14
      Counting
        Simple
        Inconspicuous
        Before and After
Microwave Detection
14

## Slide 15: Multi-lane Microwave Detector
15

## Slide 16
Triple Beam Technology
16

## Slide 17
Triple Beam Technology
17

## Slide 18
Classifications Details and Controls
18

## Slide 19: Magnetometers Detection
19

## Slide 20
SPP Digital Radio
APCC
Repeater
Sensors
      Wireless Magnetometer
20

## Slide 21
      Microloop (wired magnetometer)
More Alternatives
21

## Slide 22
      Advantages
        Wireless to cabinet
        Core drill only
        Specific point detection
        Good temporary installation features
      Disadvantages
        Complex to setup
        Limited range
        Site survey required
        Battery replacement required
        Small detection footprint
Magnetometers Detection
22

## Slide 23
Overheight Warning Break the Beam
23

## Slide 24
Overheight Warning Break the Beam
24

## Slide 25: Video Detection
25

## Slide 26: Video Detection
26

## Slide 27
      Advantages
        No diggers hotline
        Flexible zone configurations
        Lower cost than loops
        Pedestrian / Bicycle Detection
        Good zone coverage w/ single camera
      Disadvantages
        Camera Occlusion can occur
        Fixed mounting required
        Need to see for detection to work
Video Detection
27

## Slide 28
BLUETOOTH SENSOR
The Bluetooth channel is used for data transmission for a limited amount of data; the channel is efficient and cost effective. Bluetooth communication is used by mobile telephones, hands-free sets, GPS navigators and more. All these Bluetooth emitting devices leave a unique digital footprint. As the vehicles circulate the Bluetooth Sensor will pick up these signals and track the path of the vehicles. With a significant percentage of the passing vehicles providing a Bluetooth signal the sensors will provide very, very accurate traffic information.
MOBILE PHONES, GPS, PDA, HANDSFREE SETS
Bluetooth Technology
28

## Slide 29: Road Side Units – DSRC, C-V2X, with BlueTooth
29

## Slide 30: Road Side Units – DSRC, C-V2X
30

## Slide 31: Road Side Units – DSRC, C-V2X
31

## Slide 32
    Alert connected vehicles that a pedestrian has activated the crosswalk system –drivers to be on the lookout for pedestrians
Connected Vehicle Interface
32

## Slide 33: Intersection Stop Warning – Various Improvements
33

## Slide 34
Thermal Applications
Wrong Way Driver
Accurate wrong-way vehicle detection
Multiple lanes of detection
Pedestrian Crosswalk
Accurate pedestrian and bike detection
Multiple zones of detection
34

## Slide 35
Rational
A thermal sensor produces an image derived from invisible infrared waves, also, simply known as heat.
Thermal sensors detect this heat and convert it into an electronic signal which is ultimately processed to produce a thermal image that is viewable by the human eye.
What is Thermal Technology
35

## Slide 36
At night and in complete darkness
Through shadows and sun glare
In all weather conditions including fog, rain and snow
Easy set up and configuration with no road shut down necessary
24/7 fast, reliable and accurate detection
Configurable zone settings to help with troublesome layouts
Advantages of Thermal
36

## Slide 37
Initial Detection
Wrong Way Detection
Thermal Wrong Way Applications
OFF-RAMP
MAINLINE
OFF-RAMP & MAINLINE
37

## Slide 38
Pedestrian Thermal Images
Configuring a Zone
Presence
Directionality
38

## Slide 39
Passive or Active Infrared Detectors
    Pedestrian Detection Sensors
      Infrared and/or microwave sensors​
      Presence and/or motion activates crosswalk system​
39

## Slide 40
      Advantages
        Specific point detection
        Low cost
        Easy to set up
        Good versatility
      Disadvantages
        Distance limiting
        Fixed mounting required
Infrared Detection
40

## Slide 41
    Considerations
      Use of infrared (IR) technology
        Dual IR beams
          Beam break order determines directionality and system activation
    Uses
      For Vulnerable Road Users (VRUs) who may not press the push button
      Corral pedestrians
      Activation further away from crosswalk
Pedestrian Detection Bollards
41

## Slide 42
Time Clock
Activate crosswalk (or school zone) alerts during specific time periods
Time activated switch – manual scheduling inside the cabinet
Remote scheduling through cloud based software
42

## Slide 43
Pedestrian Push Buttons
Mechanical push buttons have historically been used for pedestrian system activation
Image is of a piezo, not mechanical, push button
43

## Slide 44
Push Button Improvements
Push button technology has improved over the years
  Piezoelectrical
  ADA-compliance
  Accessible
  Audible
  Touchless
  Bluetooth
44

## Slide 45
    Audible push buttons
      Notification to let pedestrians know the call has been received
      Audible messages to notify pedestrian of walk sign, or that the warning lights are flashing
    Bluetooth
      There are now products with applications on the market where pedestrian can activate signalized and unsignalized crossings
Push Button Improvements
45

## Slide 46
    Visual software is evolving to use different technologies to detect pedestrians and even predict pedestrian movements
      Extend green light time for bikes
        Also bikes can ask for green via apps
      Extended walking time for pedestrians
        Based on pedestrian density
Smart Cameras and Software
46

## Slide 47
Any Questions?

## Slide 48: Contact Information
48